## Slide 1: Applying Discrete Global Grid Systems (DGGS) across diverse data jurisdictions.
http://locationindex.org/
Joseph Bell, Geoscience Australia

## Slide 3: Different ways of describing Location
Descriptive – e.g. semantic links through place name descriptions/associations
Position & Geometry – e.g. latitude, longitude and topological relationships through classic GIS methods
Indexing – e.g. DGGS or ASGS polygons
DGGS (Discrete Global Grid Systems )

## Slide 4: Discrete Global Grid Systems (DGGS) as defined by the OGC
an earth reference system – whole Earth
hierarchical – fixed relationships between parents & child cells
equal area - cells of same resolution have equal area
tessellation of the Earth to partition and address the entire globe

## Slide 5: Several DGGS shapes but very similar principles
Tetrahedron
Cube
Octahedron
Dodecahedron
Icosahedron
Equal Area
Tessellations
of the
Earth’s Surface
Model
Simple cell
Types:
Rectangular
Triangular
Hexagonal

## Slide 6
Gibb, R.G., 2016, “The rHealPIX Discrete Global Grid System”
AusPIX Cubic model

## Slide 7: Advantages of a DGGS (AusPIX) implementation
Regular and unchanging
Ellipsoidal – no map transforms needed - excellent for continental scale
Worldwide application – not a local grid
Polar regions catered for.
Can define location to degree of resolution required eg big cells for sensitive data, small cells for high resolution.
Uncertainty can be expressed by the size of the cell
Can be used as a location index.
Ability to fuse data from multiple projections using DGGS as the consistent reference frame.

## Slide 8
Australian Region
R cells

## Slide 9
DGGS grid over a small part of Canberra. Cell are approximately 160m across. (DGGS level 10)

## Slide 10: Implementing DGGS
1. DGGS engine (eg rHealPIX, AusPIX)
2. Tagging existing data with DGGS attributes
  Points eg. addresses, place names Point (149.0766452, -35.38421273) = R7852374756
  Lines eg. roads, rivers
  Polygons eg. Statistical Areas, National Parks, Cadastre, disaster areas
  Rasters eg. satellite imagery
http://github.com/GeoscienceAustralia/AusPIX_DGGS
pn:VIC15650 pn:hasPlaceName "LOY YANG A POWER STATION" .
pn:VIC15650 pn:FeatureClassification "Built Structures" .
pn:VIC15650 pn:latitude "-38.2540278" .
pn:VIC15650 pn:longitude "146.5743056" .
pn:VIC15650 pn:State "Victoria" .
pn:VIC15650 pn:DGGSrHealpix "R787222356873"
DGGS tag

## Slide 11: Tools (under development)
DGGS to shapefile – visualisation, verification
Github repository
http://github.com/GeoscienceAustralia/AusPIX_DGGS
Figure 3; Belconnen SA2 with level 10 (140m) DGGS Polygons and centroids.

## Slide 12: Future work:
  On the fly DGGS tagging (compared to imbedded tagging)
  Complete DGGS tagging script for lines and rasters
  Methods to walk between DGGS instances and types
  User interfaces (UI’s) to integrate data based on DGGS taggs
  Develop output types, eg csv, shapefiles, RDF triple-store etc

## Slide 13: Implementing Data integration
Integrate data using the DGGS tags
  Simple network of methods to suit different workflows
  1) Simple UI based – less flexible
  2) Complex – special tools based – but flexible, eg Sparql queries in triple stores

## Slide 14: Connecting data using DGGS as a Location index
Place Names
Digital Elevation Model
Australian Bureau of Statistics SA2
“Acacia Inlet” is at an elevation of 554m and is located in
SA2 code 801061066
All hyperlinks to landing pages that include map and attributes for those features.

## Slide 15: DGGS tagged triple store
Triple-store that connects Place Names to their DGGS reference tags. (draft)

## Slide 16: Start to answer questions like:
For a flood disaster:
What are the Location Index cells that represent that area [e.g. DGGS]?
Where are the low areas in this region? [DEM]
How many people could be affected, how many addresses? [ ASGS Mesh Blocks]
What government support might be needed (population statistics, age, economics) [DHS, DSS data]
What is the impact on agriculture/industry [economic and productivity data]
What assets (natural or economic) are in the area [Dept Ag, Dept Environment]
What support structures are nearby (Hospitals, Fuel stations etc)
Tech. Sgt. Rachelle Blake/U.S. Air Force via AP